## Slide 1: Rainfall sensor Update
Keith Matthews

## Slide 2: Data
USGS only registered 0.02 in rainfall event
USGS records rainfall for every quarter hour
Very windy
Increase sample size decrease the sample rate
Chart: Rainfall
Rainfall event ( per USGS) | 1000 | 870
Temperature | 79 | 81 | 81 | 82 | 84 | 84 | 84 | 82 | 79 | 79 | 77 | 77 | 77 | 77 | 73 | 66 | 63 | 61 | 59 | 57 | 55 | 55
Chart: Enviromential Conditions
| 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Humidity (%) | 79 | 74 | 74 | 70 | 62 | 66 | 66 | 70 | 79 | 79 | 83 | 83 | 83 | 57 | 50 | 52 | 59 | 59 | 63 | 67 | 72 | 72
Temperature (F) | 79 | 81 | 81 | 82 | 84 | 84 | 84 | 82 | 79 | 79 | 77 | 77 | 77 | 77 | 73 | 66 | 63 | 61 | 59 | 57 | 55 | 55
Wind (MPH) | 19 | 12 | 12 | 12 | 15 | 12 | 12 | 14 | 12 | 11 | 11 | 12 | 12 | 16 | 17 | 19 | 12 | 15 | 9 | 11 | 8 | 8
Pressure | 1006.8 | 1006.9 | 1006.2 | 1005.1 | 1004.3 | 1003.4 | 1002.9 | 1002.7 | 1002.8 | 1003 | 1002.4 | 1001.9 | 1001.4 | 1001.7 | 1003.4 | 1005.3 | 1006.2 | 1007.3 | 1008.1 | 1008.8 | 1010.7 | 1012.2

## Slide 3: Redesign top piece
Deformation internal electrode holder
  Due to heat
  Make thicker and connect
Reciprocal Function
  V=IR = I*(1/H)
  Flatten the curve
    Increase the current
    Angle the electrodes?
Chart: 

## Slide 4: New top
Issues
  Want resolution
  Want a better capture ratio
    Disrupted due to wind and drone docking port
Funnel intake
  Increase SA?
    Better for wind events
  Reduced Height?
Magnetic mount area
  Ferrous steel
  400 grade SS
  Mesh

## Slide 5: New top
Reduced overall height (reduction of 40mm)
Easier assembly
Internal wiring
More accurate data (ratio of ~16:1)

## Slide 6: Capacitance
Starting capacitance of 11.2768 pF (for rainfall of 0.01 in at a separation of 1mm)*
Issue: Arduino can measure down to 100 nF*
How to fix the issue
  Different circuit?
  Increase intake ratio
  Change to PCB sensor (coat with a material)

## Slide 7: Thoughts, Question, or Advise?