## Slide 1: Water probe and Rainfall sensor Update
Keith Matthews

## Slide 2: Rainfall sensor
Case
Electronics
Issues
  Vibrations
  Increased variance during the day
  Out of range

## Slide 3: Piezoelectric Rainfall sensor
Conversion Factor
Piezo: measurement mV
  Deflection- caused by Force
Need “Velocity” – inches per hour
Mathematical(ish)
  Voltage = Energy per electrical charge ~ Energy (constant amperes)
  Voltage ~ K.E. = (assume terminal velocity)
  Velocity
Statistically
  Linear Regression:

## Slide 4: Auto righting
It is auto righting!

## Slide 5: Waterproof
Mostly: only one leak
Small imperfection in base print causing leak
Higher quality prints take days
  Still not guaranteed
Waterproof Electronics box

## Slide 6: Measuring Nitrates
Chemical Test: Ring Test (iron(II) sulfate and sulfuric acid)
In Situ with UV absorption?
  Servo: to move the diffuser
  Monochromator
  Source (Sun?)
  Detector (photosensor)
Measurement range
Detect other materials in the water?
Angle determines the wavelength
Monochromator

## Slide 7: Next Steps
Rainfall
  Case V1
  Regression Equation
  Mounting System
Water Probe
  Case V3
    Field testing
  Test Sensor System

## Slide 8: Sources
https://pubs.rsc.org/en/content/articlelanding/2018/en/c8en00588e#!divAbstract
http://www.pitt.edu/~asher/homepage/spec_pdf/UV%20Resonance%20Raman%20Spectroscopic%20Detection%20of%20Nitrate.pdf
https://www.shimadzu.com/an/uv/support/fundamentals/monochromators.html

## Slide 9: Dissolved Oxygen

## Slide 10: Battery
Samsung cylinder batteries?
  Stackable
  Flexible design
  One charger for all
LiPo
Charging?
Replacing

## Slide 11: Table of Parameters

## Slide 12: Package Conditions
Over water
Water Height
Algae
In Water
pH
TDS
Open Air
Rainfall
Other?
Physical Samples
More

## Slide 13: 3 packages
Above water package
  Currently the water height sensor package
  Add camera for algae machine vision detection capabilities
In water package
  Under development
Open air package
  Testing/development

## Slide 14: Probe Swap
Easier
Eliminates Docking